## Slide 1: ENUM successes – failures - alternatives
RIPE 64, April 18 2012, Ljubljana (SI)
Alexander Mayrhofer
<alexander.mayrhofer@enum.at>

## Slide 2: ENUM – ecosystem components
The „Protocol“
  Core protocol
  Enumservice definition
  IETF WG
ENUM „Flavours“
  User ENUM
  Infrastructure ENUM
  Private ENUM

## Slide 3: ENUM – ecosystem components II
User ENUM:
  The „e164.arpa“ administration
    Globally (RIPE‘s „root“ role)
    ITU „interim procedures“
    Locally (+43, ..)
    Interaction with Regulators
  The community
    Local interaction
    ENUMfederation

## Slide 4: „Core“ Protocol + IETF WG
RFC2916 (2000) -> RFC3761 (2004) -> RFC6116 (2004)
Stable, deployed
  (but still „proposed standard“)
  Late (interesting!) alternative of the „URI RRType“.
IETF WG closed in May 2011
SUCCESS!

## Slide 5: Enumservice Registration
IANA registry defined in
  RFC2916 – not!
  RFC3761 – IESG approval, RFC publication
  RFC6117/8 – Specification Required (eases registration independent of WG existance)
Currenty 40 services (type/subtype) registered
TODO: most popular services?
SUCCESS!

## Slide 6: User ENUM – Implementation (Registries part)
Registration of ENUM-Records in publicly available DNS, under control of the End User
  e164.arpa administration: RIPE „root“, ITU „interim procedures“
    SUCCESS! (besides some lame delegations)
  *.e164.arpa administration: Implementation of registry in accordance with local regulators
    SUCCESS!
  ENUM Validation: Complex and resource intensive process
    FAILURE (too complex in the „user control“ scenario)

## Slide 7: User ENUM – industry uptake
Some very eager early adoptors
  Mostly small VoIP operators
  Zero large Telcos (User empowerment, „free calls“ just scary to them)
Criticial mass never reached
  Left early adoptors frustrated
  „Eager Operator“ report: ENUM „call rate“ below 1%, „ENUM minutes“ by magnitudes more expensive
„It‘s not about free calls, it‘s about new services“
  Never happened – „Skype just works fine for me“
  Minutes are cheap anyway – fixed -> mobile
FAILURE

## Slide 8: Current uptake
http://crawler.enum.at
  900k numbers globally (800k in Taiwan??)

## Slide 9: Infrastructure ENUM
Operator-controlled entries in the public DNS
Response to „user control is bad, we still want to use ENUM for the peering case“
  Once in operation, they went silent
  Zero uptake in +43
  Any uptake elswhere
FAILURE – why?
  Those willing already had user ENUM in place
  Operators don‘t want to expose their data, market share, infrastructure
  Chicken/Egg problem in VoIP-peering – ENUM solves only the „discovery“ problem

## Slide 10
So, where‘s the success?
it‘s invisible.
It‘s not on the internet.
It‘s „private ENUM“

## Slide 11: Private ENUM
The use of ENUM-Technology in private environments
  Accessible from within an operators network only
  Or within a group of operators
  Or in form of a „VoIP peering point“
Massive uptake in most VoIP operator networks
SUCCESS!

## Slide 12: Private ENUM use cases
Peering Scenario: Find peer organisation for a certain number
Local Number Portability queries
Caller Name queries
Internal routing queries
Selecting an outbound „trunk“ from within a network
ENUM is still the prime (only?) standardized E.164 -> identifier lookup protocol

## Slide 13: Private ENUM success reasons
Implemented in almost any vendor‘s VoIP switch (even in some IMS equipment..)
DNS is well understood, scales extremely well, and supports high query loads
Private ENUM does not expose data „outside“
Allows use of „non-standard“ Enumservices
  And even „hacks“ in the DNS, like client-specific answers

## Slide 14: Alternatives – User ENUM
For individuals:
  Skype, mobile phone, Instant Messaging
  Phone numbers are not *that* important anymore (Smartphones)
  And calls are cheap – normal phones *are* and alternative
  ENUM requires information to be public – hinders „service discovery“ and „business card“ cases
  P2Psip?

## Slide 15: Alternatives – User ENUM
For enterprises:
  Vendor-specific „PBX interconnect“
  Least Cost Routing – calls are cheap
  ViPR – http://tools.ietf.org/wg/vipr
    „Built-in“ validation (via PSTN)
    „Build-in“ discovery of numbers (DHT)
    „New services“ rather than „free calls“ (sounds familiar ;)

## Slide 16: Alternatives – Infrastructure ENUM
Bilateral agreements, employing private ENUM (if at all)
Managed „VoIP Peering Fabrics“
http://tools.ietf.org/wg/drinks
  Provisioning protocol for VoIP peering data
  Doesn‘t require the „output“ to be (i/p)-ENUM
  But supports NAPTRs

## Slide 17: Conclusion
User-ENUM: Too complex, financially unattractive, overtaken by other services
Infrastructure-ENUM: embraced only by smaller operators, scary to larger ones, solves only part of the problem (discovery)
Private ENUM: Success – at least makes use of the protocol and the services registration, but does not require the administrative infrastructure of e164.arpa…